## Slide 1: Computer Architecture
Lecturer-in-charge: K.P.N Jayasena

## Slide 2: Objectives
At the end of this lecture you will be able to explain
  The basic structure of a computer and its main components
  Elements of CPU
  Bus architecture
  How CPU and its components work

## Slide 3: Agenda
Von Neumann Architecture.
The main components of a computer.
Bus Architecture.
CPU, its elements and functioning.
Fetch-Execute Cycle
Notes: 3

## Slide 4: Hard Wired Programming
Early computers were programmed, using large number of switches in the console panel and plugging/unplugging cables
It is called hardwired programming
Notes: ENIAC ( Electronic Numerical Integrator And Computer)[1][2] was the first general-purpose electronic computer)
4

## Slide 5: John Von Neumann
It was required re-wire and re-design the machine to run a
different programs. It was a manual and very tedious task
Von Neumann proposed that programs and data can be stored in a memory device and instead of rewiring the machine we can change the program easily. (Stored Program Concept)
Notes: 5

## Slide 6: Von Neumann Architecture
Important Components
Notes: 6
von Neumann Architecture. John von Neumann elucidated the first practical stored-program computer architecture (scheme for connecting computer components) in the mid-1940s. It is comprised of the five classical components (input, output, processor, memory, and datapath). The processor is divided into an arithmetic logic unit (ALU) and control unit, a method of organization that persists to the present. Within the processor, the ALU datapath mediates data transfer for computation. The registers are fast memory modules from/to which data can be read/written to support streaming computation, as shown in Figure 1.8. Within the ALU, an accumulator supports efficient addition or incrementation of values corresponding to variables such as loop indices.

## Slide 7: Von Neumann Architecture
The use of the binary number system
A single sequentially addressed memory
A separate arithmetic/logic unit for performing arithmetic and logical computations
The stored program concept in which both the programs and its data are stored in memory.
A controller that fetches instructions from memory and executes them.

## Slide 8: Main Components of a Computer
CPU
Main Memory
I/O Modules
Interconnections (buses)
Notes: 8

## Slide 9: Main Components of a Computer
Notes: 9

## Slide 10: CPU
CPU is like the brain of the computer.
Main functions:
  Fetch data and instructions from memory.
  Coordinate the complete execution of each instruction.
Main Components of the CPU
  ALU (Arithmetic and Logic Unit).
  Control Unit.
  Registers.
Notes: 10

## Slide 11: Memory
The memory is a collection of storage cells, each of which can be in one of the two states.
One state represents a value “0” and the other represents a value of “1”.
By distinguishing these two different logical states, each cell is capable of storing a single binary digit, or bit, of information.

## Slide 12: Primary Memory
Primary storage or memory: Is where the data and program that are currently in operation or being accessed are stored during use.
  Consists of electronic circuits: Extremely fast and expensive.
  Two types:
    RAM (non-permanent)
      Programs and data can be stored here for the computer’s use.
      Volatile: All information will be lost once the computer shuts down.
    ROM (permanent)
      Contents do not change.

## Slide 13: Input output modules
Input output modules interface the Computer system to the input output devices.
  Video controller
  SCSI disk controller
These modules enable program and data to be entered to the system.
In CPU’s perspective there is no difference between the way of accessing the memory and the input out modules.

## Slide 14: I/O Module Connections
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer
Notes: 14

## Slide 15: Buses
A communication pathway connecting two or more devices
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Buses carry data, instructions and control signals.
Notes: 15

## Slide 16: Structure of the CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU
Notes: 16

## Slide 17: ALU
Combines and transforms the data using
  Arithmetic operations (+, -, /, *)
  Logical operations (bit-wise negation, AND , OR)
The results of an arithmetic-logic unit operation are usually transferred to the accumulator.
Lecture 07 – Computer Organization – Part I

## Slide 18: Accumulator
A register located on the central processing unit.
The contents can be used by the ALU for arithmetic and logic operations, and by the memory buffer register.
Usually, all results generated by the arithmetic-logic unit end up in the accumulator.

## Slide 19: Accumulator
Example: Say ALU would perform NOT operation on data in its accumulator as shown below.
Lecture 07 – Computer Organization – Part I
Accumulator before ALU perform the NOT operation |  |  |  |  |  |  | 
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Accumulator After ALU perform the NOT operation |  |  |  |  |  |  | 
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 20: Control Unit
Control unit is the nerve center of the computer. (brain with in the brain)
It coordinates and controls all the hardware operations.
(i.e. that is all the peripheral units and the CPU itself).
Control units fetches instructions from the memory, decodes it and gives control signals according to the instruction.

## Slide 21: Registers
A register is a discrete, high speed memory location within the CPU designed to hold temporary data, instructions or results.
A modern CPU will hold a number of registers.
1 . General purpose registers.
Ex: AH,AL,BH,BL
2. Special purpose registers
Ex: Control registers, flag registers

## Slide 22: Control Registers of the CPU
  Programme Counter(PC)
    Contains the address of the next instruction to be fetched
  Instruction Register(IR)
    Instruction most frequently fetched
  Memory Address Register(MAR)
    Address of a location in memory
  Memory Buffer Register(MBR)
    Contains a word of data to be written to memory or the word most recently read
Notes: 22

## Slide 23: Control Registers : Program Counter Register(PC)
Before the CPU can execute an instruction, the instruction must first be brought to the CPU from the computer‘s memory.
PC register contains the memory address of the next instruction to be executed.
After fetching of an instruction is completed program counter is incremented by one.
[PC] 🡨 [PC] + 1

## Slide 24: Control Registers: Memory Access Register(MAR)
Fetching an instruction begins with the program counter being moved to the memory address register (MAR).
    [MAR] 🡨 [PC]
This register locates in the CPU and in turn connect to address bus.
Specifies the address in memory where information can be found and can be also used to point to a memory location where information is to be stored.

## Slide 25: Control Registers: Memory Data Register(MDR)
A register located on the CPU which is in turn
connected to the data bus of the system.
Also known as Memory Buffer Register (MBR).
The memory location stored in the memory address register is used to copy data from or to the memory buffer register.
Examples …

## Slide 26: Control Registers: Instruction Register (IR)
IR is the part of a CPU's control unit that stores the instruction most recently fetched.

## Slide 27: Status Registers(Flag Registers)
The status register is a hardware register which contains information about program state.
Takes the snapshot of state of the ALU after each instruction is executed.
The CPU updates the bits of the status register after it carries out arithmetic or logical operation to reflect the nature of the result.
Notes: 27

## Slide 28: Status Registers(Flag Registers) cnt...
  Bits of the status register could be ,
  Sign: sign bit of the result of the last arithmetic operation
  Zero: set when the result is zero
  Carry: set if an operation resulted in a carry
  Equal: set if a logical compare result is equality
  Overflow: used to indicate arithmetic overflow

## Slide 29: Buses
A communication pathway connecting two or more devices
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Buses carry data, instructions and control signals.
Notes: 29

## Slide 30: CPU with System Bus
A Bus is a communication pathway two or more devices
Notes: 30

## Slide 31: System Bus
What is this ROM(will be discussed later)
Notice the direction of buses.
Notes: 31

## Slide 32: Bus Architecture
Notes: 32

## Slide 33: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width of a bus is a key determinant of performance
  8, 16, 32, 64 bit
Bi-directional
Notes: 33

## Slide 34: Address Bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space
If the width of the address bus is 32 what is the maximum addressable memory ?
Uni-directional
Notes: 34

## Slide 35: Control Bus
It is used to transmit a variety of individual signals (read, write, interrupt, acknowledge) necessary to control and coordinate the operations of the computer.
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals
Bi-directional
Notes: 35

## Slide 36: CPU Functions
Fetch instructions
Execute instructions
    Interpret instructions
    Fetch data
    Process data
    Write data
Notes: 36

## Slide 37: Instruction Cycle
All computers have an instruction cycle.
A basic instruction cycle can be broken down into the following steps:
  Fetch cycle - Fetch an instruction
  Decoding
  Execute cycle - execute an instruction

## Slide 38: Fetching Cycle
  PC contains address of next instruction
  Address moved to MAR
  Address placed on address bus
  Control unit requests memory read
  Result placed on data bus, copied to MBR, then to IR
  Meanwhile PC incremented by 1
Notes: 38

## Slide 39: Data Fetch
Notes: 39

## Slide 40: Fetch the Instructions
Ins-1
B5
13
AC
A109
A108
A107
003
002
001
Memory
Control Unit
PC
MAR
002
MBR
002
Ins-1
Ins-1
IR

## Slide 41: Decoding
After the fetching an instruction, the CU checks the contents of the IR and determines which type of execution is to be carried out next.
This process is known as the decoding phase. The instruction is now ready for the execution cycle.
Decoding the opcode in the instruction register includes following:
  Determining the instruction
  determining where its operands are in memory
  Retrieving the operands from memory
  Allocating processor resources to execute the coomand

## Slide 42: Instruction Formats
0
Address of the operand
3
4
15
Opcode
Notes: 42

## Slide 43: Execute Cycle
The actions within the execution cycle can be categorized into the following four types of operations:
CPU - Memory: Data may be transferred from memory to the CPU or from the CPU to memory.
CPU - I/O: Data may be transferred from an I/O module to the CPU or from the CPU to an I/O module.
Data Processing: The CPU may perform some arithmetic or logic operation on data via the arithmetic-logic unit (ALU).
Control: An instruction may specify that the sequence of operation may be altered.

## Slide 44: Instruction Cycle State Diagram
Notes: 44

## Slide 45: Fetch the Data
Ins-1
78
13
AC
A109
A108
A107
003
002
001
Memory
78
Control Unit
MAR
A107
MDR
78
Accumulator
100
(We want to add data stored in location A107 to ACC)
xxxx|xxxxxxxx
IR
178
Notes: 45

## Slide 46: Fetch the Data
Ins-1
78
13
AC
A109
A108
A107
003
002
001
Memory
78
Control Unit
MAR
A108
MDR
100
Accumulator
100
(We want to write data stored in Accumulator to A108)
100
xxxx|xxxxxxxx

## Slide 47: Data Fetch
IR is examined(Decoding)
If indirect addressing has been used
  Right most N bits of MBR transferred to MAR
  Control unit requests memory read
  Result (address of operand) moved to MBR
Notes: 47

## Slide 48: Registers
A register is a single permanent storage location within the CPU used for a particular purpose.
• Examples of registers:
      – Program counter (PC)
      – Instruction register (IR)
      – Memory address register (MAR)
      – Memory data register (MDR)
      – Accumulator (ACC)
      – Status register
• General purpose registers
      – Included on some CPUs
      – Used for high-speed temporary storage

## Slide 49: Program Counter ( PC )
A dedicated register in the CPU.
Contains the address in memory of the current instruction being executed.
Incremented automatically after each instruction.
Usually initialize to zero when machine starts, or is reset.

## Slide 50: Instruction Register ( IR )
A dedicated register in the CPU which contains the actual current instruction
Op Code + Address
What To Do
Location of Data
Simple 16-bit example:
1101 101101100100
Notes: 50

## Slide 51: Memory registers
Memory Address Register (MAR)
Contains Address in memory to find or place data.
Memory Data Register (MDR)
Contains Actual Data to be placed in location given in MAR, or which has been retrieved from location given in MAR.

## Slide 52: Accumulator
A dedicated register (or set of registers) in the CPU used for the actual manipulation of data.
Default source (or destination) register.
Usually contains results of arithmetic or logical
operations.

## Slide 53: Generic CPU With Registers

## Slide 54: Fetch-Execute Cycle
• Two steps, or cycles, in the execution of
every instruction
– Fetch
fetch the code for the instruction from
memory and place it in the IR (instruction
register)
– Execute – execute the instruction

## Slide 55: The LOAD Instruction
PC -> MAR
Transfer the address from the PC to the MAR
MDR -> IR
Transfer the instruction to the IR
IR(address) -> MAR
Address portion of the instruction loaded in MAR
MDR -> A
Actual data copied into the accumulator
PC + 1 -> PC
Program Counter incremented

## Slide 56: Store Fetch/Execute Cycle
PC -> MAR
Transfer the address from the PC to the MAR
MDR -> IR
Transfer the instruction to the IR
IR(address) -> MAR
Address portion of the instruction loaded in MAR
A -> MDR*
Accumulator copies data into MDR
PC + 1 -> PC
Program Counter incremented

## Slide 57: The Add Instruction
PC -> MAR
Transfer the address from the PC to the MAR
MDR -> IR
Transfer the instruction to the IR
IR(address) -> MAR
Address portion of the instruction loaded in MAR
A + MDR -> A
Contents of MDR added to contents of accumulator
PC + 1 -> PC
Program Counter incremented

## Slide 58: Fetch-Execute Example: Load Accumulator
Assume: Simple Eight bit system.
Thirty-two memory locations (0 to 31).
“Load” instruction is 010.
Value in location 15 is ten (ie: binary 00001010)
PC is at 5, about to increment.
The instruction, 01001111, is in location 6

## Slide 70
Now:
Assume: Value in location 7 is 10110010.
“ Add” instruction is 101.
Value in location 18 is seventy- one
(i.e.: binary 01000111)